## Slide 1: VELKOMMEN TIL BILDEBANKEN MED FOKUS PÅ BARN OG TAI!
Her er et utvalg bilder som kan hjelpe til med å skreddersy TAI-instruksjonene til hvert barn. Målet er at alle barn skal kunne utføre TAI selv.
Du velger rett og slett bilder med barnet eller barna som du tror barnet best kan identifisere seg med. Deretter lager du en serie bilder med akkurat de tingene pasienten din bør trene på.
Vi håper disse bildene vil være til stor hjelp for å lære barn å irrigere seg selv ved hjelp av Navina-irrigasjonssystemet.

## Slide 2: Slik fungerer tarmen og TAI
Notes: How the bowel works
Navina Smart
Navina Classic

## Slide 3: Forberedelse for TAI
Notes: Open door
Turn on the lights
Wash hands

## Slide 4: Forberedelse for TAI
Notes: Take of the pants, toilet
Take of the pants, wheelchair

## Slide 5: Forberedelse for TAI
Notes: Take of the pants, toilet
Take of the pants, wheelchair

## Slide 6: Forberedelse for TAI
Notes: Take away incontinence protection
Bag

## Slide 7: Flytting
Notes: Lock the wheelchair
Move to the toilet
Move to the wheelchair

## Slide 8: Flytting
Notes: Lock the wheelchair
Move to the toilet
Move to the wheelchair

## Slide 9: Sett inn kateteret/conen
Notes: Insert the catheter into the rectum from the front
Insert the cone into the rectum from the front

## Slide 10: Sett inn kateteret/conen
Notes: Insert the catheter into the rectum from behind
Insert the cone into the rectum from behind

## Slide 11: Sett inn kateteret/conen
Notes: Insert the catheter into the rectum from the front
Insert the cone into the rectum from the front

## Slide 12: Sett inn kateteret/conen
Notes: Insert the catheter into the rectum from behind
Insert the cone into the rectum from behind

## Slide 13: Forbered Navina Classic
Notes: Fill the water container with lukewarm clean tap or bottled water
Connect the tube with dark blue connectors to the dark blue connector on the water container.
Lock the connection by turning it clockwise until it stops

## Slide 14: Forbered Navina Classic
Notes: Connect the tube with the light blue connector to the light blue connection.
Lock the connection by turning clockwise until it stops.
Connect the tube with the white connector to the catheter/cone.
Lock the connection by turning it clockwise until it stops.

## Slide 15: Forbered Navina Classic
Notes: Open the water flow and use the dark blue pump to start the water flow
Water to activate the hydrophilic surface of the cone
Water to activate the hydrophilic surface of the catheter

## Slide 16: TAI med Navina Classic
Notes: Use the grey pump to inflate the balloon
Pump water into the bowels with the blue pump
Pump water into the bowels

## Slide 17: TAI med Navina Classic
Notes: Empty the balloon

## Slide 18: Tarmen tømmes
Notes: Wait to poop, play games
Empty the bowels
Empty the bowels

## Slide 19: Etter å ha fullført TAI
Notes: Wipe the butt
Insert incontinence protection
Insert incontinence protection

## Slide 20: Etter å ha fullført TAI
Notes: Move to the wheelchair
Move to the wheelchair

## Slide 21: Etter å ha fullført TAI
Notes: Flush the toilet
Wash hands

## Slide 22: Demontering og rengjøring
Notes: Disconnect tubes from control unit
Disconnect tubes from control unit
Disconnect the catheter/cone and dispose in household waste

## Slide 23: Supplerende bilder
Notes: Extra
Schedule irrigation regularly at a time during the day that suits the child's schedule.